# EDUCATION & TRAINING DIVISION

### FIREARMS SECTION

SAFETY & MAINTENCE

# Introduction:

An officer is responsible for the proper storage of his service weapon at all times.  Should the weapon be used by an unauthorized person and injury results, the officer can be held accountable from a departmental and/or civil standpoint.  An officer must know and practice proper safety and storage procedures.

Also, an officer must know how to properly field strip, clean and reassemble the Glock and its magazines to insure positive operation of the weapon.

- Safe Handling and Storage of the Glock 22.

A.	The four Cardinal Rules of Firearm Safety       (Obj.170)

- All guns are loaded.

- Point the muzzle in a Safe Direction.  The “Laser Rule”.

- Keep your fingers outside the trigger guard until you are on target and have decided to fire.

- Be sure of your target and what is around and beyond it.

- Basic Safety considerations

- The pistol is not an impact tool: Avoid striking anyone or anything with it.

- Do not engage in locker room “Quick Draw” contests.

- Do not play “Show and Tell”.

- Do not point the firearm at anyone/anything unless the situation would allow you to pull the trigger.

- Do not hand a loaded firearm to or receive a loaded firearm from anyone.

- Explain the safe way to hand a firearm to another.

- Magazine removed

- Slide is locked back/open

- The unloading procedure will be covered in this lesson

plan, Section II.

- The reasons for removing the pistol from the holster are:

- Confrontations which involve the imminent threat of

force or serious injury to the officer or others.

- Practice at the range.

- Cleaning

- Inspection

- Storage

- Armorer Repair

C.	Safety and Storage at Home                  (Obj. 172)

- “When not in use firearms shall be kept in a secure place

inaccessible to persons not members of department.”*

*looks like a toy gun

- Out of the reach of children.

- In a secured container or place.

- Avoid obvious storage locations.

- with jewelry

- bedside table

- under mattress or pillow

- Safe Storage

- Unload firearm before storage.

- Store ammunition separately.

- Remove the slide from receiver.

- Trigger locking devices such as padlocks or handcuffs may damage the trigger safety.

- Cable lock.

D.        Moving with Pistol in Hand

- Point the weapon in a safe direction.

- Keep the trigger finger at touchpoint.

- Field Stripping Exercises*

- Unload the weapon

- Hold the weapon in strong hand by grips; finger off the trigger

and outside the trigger guard.

- Point weapon in a safe direction. (Laser Rule)

- Press and hold magazine catch.

- Right hander – use right thumb to press and hold

magazine catch.

- Left hander – use left index finger or thumb to press

and hold magazine catch.

4.        With the support hand, grasp the magazine by the floor plate

and pull out of the magazine well.  Put the magazine down.

5.	Grip the grasping grooves located on both sides of the rear of

the slide firmly with support hand:

- Right Handers – place the left hand over the slide with

the pads of the fingers on one side of the slide and the heel of the palm on the other side – Caution – keep fingers clear of the ejection port.

- Left Handers – place the right hand over the slide with

the thumb stretched straight along the left side of the slide and the pads of the fingers on the other side with the fingers clear of the ejection port.

6.	Both right and left handers hold the slide firmly with support

hand and push forward on the grip ejecting any ammunition in the chamber.

- With the chamber open engage the slide stop:

- Right Hander – Use right thumb to push slide stop up.

- Left Hander – Use the right thumb to push slide stop up.

- Keep weapon pointed in safe direction and visually inspect the

chamber and magazine well to ensure that weapon is  unloaded. *

*LOOK, LOOK AWAY, and LOOK AGAIN.

- Release the slide into battery.

- Firmly grip the grasping grooves between thumb and

index finger of support hand; pull slide sharply to the rear and release.

- Alternate Method – press the slide stop down with the

thumb of the strong hand.  (Note; used only if the officer is injured and can not release slide into battery as described above)

- Field Strip the Weapon

- Insure that the weapon is unloaded by following procedure

above (II.A.) * Look, Look Away, Look Again. (Obj. 166)

- Release the slide into battery by manipulating the slide as

described above (II.A.10.)

- Point the weapon in a safe direction and pull the trigger to the rear.

- Place the web and thumb of the strong hand on the rear of the receiver just below the back of the slide with fingers of the strong hand wrapped over the top of the slide.

- With the fingers, pull the slide back about 1/10 of an inch, hold the slide in this position.

- Bring the support hand, palm up, to a position under the receiver (in front of the trigger guard) and place the thumb on the slide lock on one side of the receiver and the index finger on the slide lock on the other side of the receiver.

- Pull the slide lock down with both the thumb and the index finger, simultaneously. *

*Keep the weapon pointed in a safe direction throughout the field stripping exercise.

- While holding the slide lock down with thumb and index finger

of support hand, use the strong hand to push the slide forward until it separates from the receiver. *

*The recoil spring and tube under pressure-hold them in place with the strong hand finger as the slide and receiver separate.

- Put the receiver down and use both hands to carefully remove

The recoil spring and recoil tub by placing your hand over the recoil spring and holding it down while applying pressure to the recoil spring tube bushing, gently pushing it toward the muzzle area of the slide until it is free.  Remove the recoil spring and tube from the slide.  Pull the tube out of the spring. *

*Depending on the date of manufacture.

- Grasp the breech end if the barrel and push slightly forward

And lift it out of the slide.

- Field stripping of the weapon is complete. *

*Depending on the date of manufacture.

- Field Stripping the Magazine

- Squeeze magazine tube in the center part of each side near the

Magazine floor plate, maintain pressure. *

*On newer magazines the reinforcement plate must be depressed first

- Push the magazine floor plate forward until it separates from

The magazine tube.  CAUTION; the magazine spring is under tension.  Hold magazine spring down while removing the magazine floor plate to prevent magazine spring from flying out the magazine tube.

- Remove magazine spring with follower attached from

magazine tube.

D.	Maintenance				(Obj. 166)

- Using a dry bore brush clean the bore and the chamber.

- Dip the bore brush into powder removing solvent and clean the bore and chamber again.

- Using a brush dipped in solvent* remove all deposits from around the breech of the barrel, the chamber, extractor, slide rails and adjacent areas.

*Solvent should not be allowed to contact sights, it may damage them.

- The ejector should be inspected to insure no visible

damage.

- Using the slotted tip rod and clean patches remove the solvent

from the bore.

- Wipe all areas clean with a clean dry cloth and patches.

- Remove any reside from the receiver with clean dry cloth, patches and/or a nylon brush.

- Lubricate

*Do not over oil the pistol.  One drop of oil on a patch.

*a.	One drop of oil wiped over outside of barrel, including,

barrel hood, muzzle end of barrel and barrel lugs.

*b.	Light film of oil on area where barrel hood rubs inside

top of slide, ahead of ejection port and slide rails.

*c.	One drop of oil to cover all four rail positions on the

receiver assembly.

*d.	One drop of oil on a patch and ran inside the barrel.

(Note:  Excessive oil could increase chambers pressure which

will damage the weapon and could lead to injury)

<<The Connector>>

*e.	One drop of oil at right rear of trigger bar.

*f.	Wipe off exterior of receiver and magazine with a

patch, slightly dampened with firearms solvent.

*Do not over oil pistol. One drop of oil on a patch.

- Weapon must be cleaned in this manner after every firing and

at least once a month. (EMPHASIZE THIS)

E.	Reassembly and Inspection of Weapon                  (Obj. 166)

- Hold the slide upside down pointed in a safe direction.  Place

muzzle end into barrel guide of slide permitting the end of barrel hood to fall into place in the slide.

- Place recoil spring tube inside of recoil spring. *

*Depending on the date of manufacture.

- while holding recoil spring and tube, carefully place small end

of recoil tube into recoil tube guide.

- Carefully compress recoil spring until recoil spring tube bushing seats into barrel lug. *

*Back end of the recoil spring tube rests in the half bottom of the barrel lug.

- While holding receiver in upright position with strong hand,

place slide upright in support hand. Barrel end of the slide and forward end of receiver should be pointed in the same direction.

- Place rear end of slide into front end of receiver making sure the rails of the slide line up with front rail guides of receiver.

- Using a push pull method push receiver forward while pulling slide to rear until slide locks into receiver.

- With weapons in strong hand use support hand to operate slide back and forth to ensure proper orientation and to spread oil.  (Do Not Over Oil)

- Disassemble and reassemble pistol in (1) one minute.

- Reassembly of Magazine

- Holding magazine tube, bottom-up, in one hand and

magazine spring with follower in other hand, insert spring, follower end first, into magazine tube. *

*The spring cannot be inserted backward

- Push the magazine spring down and hold it in the

magazine while slipping the magazine floor plate on the bottom of the magazine tube. *

*The magazine floor plate is open only at one end and cannot be slipped on backwards.

F.	 Inspection and Function Testing Procedures (Obj. 166)

- Unload pistol and magazines, perform “Condition Check”

(WEAPON WILL NOT BE FIELD STRIPPED).

2.	Inspection Procedures:	inspect pistol and magazine

visually and by touch to insure that they are free of excessive

oil, any dirt, lint, powder or obstructions.

- Pistol

- Chamber

- Feed Ramp

- Under Extractor

- Bolt Face

- Firing Pin Orifice

- Barrel (interior and exterior)

- Magazine Well

- Ejector (for damage)

- Magazine

- Magazine Tube

- Magazine Follower

- Magazine Well

- Magazine Floor Plate

- Magazine Lips (for damage)

3.	Function Testing and Glock Pistol and Magazines    (Obj. 166)

- If the pistol or magazine fails any Function Testing

Procedures, have it serviced by the departmental Armory.

- DO NOT return the pistol or magazine to service until

the Armory has corrected the malfunction.

- Function Testing the Recoil Spring – rack the

slide forcefully several times, the slide should snap forward into battery: ejection port closed, recoil spring tube flush with slide and rear of slide flush with slide and rear of slide flush with rear of receiver.

- Function Testing the Slide Stop Level – pull the

slide to the rear and engage the slide stop level.  Press the slide stop level down and the slide should return to battery.  While the slide is forward, press the slide stop lever up and release it.  The lever should spring back down.

- Function Testing the Trigger Safety – with slide

in battery and weapon pointed in a safe direction

place the thumb and index finger on the sides of the trigger rearward.  Proper trigger safety function will prevent the trigger from being pulled completely to the rear.

- Function Testing the Trigger Pull – with slide in

battery and weapon pointed in a safe direction place the trigger in the fire position.  Pull the trigger slowly to the rear and the trigger safety will disengage.  As the trigger continues to travel a noticeable resistance will be felt as the trigger approaches the fire position.  An audible click will be heard as the trigger releases the firing pin forward.  The trigger will remain in the rearward position until the slide is racked back and trigger is released.

- Function Testing the Magazine (follower, spring,

tube and floor plate) – compress the magazine spring by pushing the follower down and releasing it.  The magazine spring should snap the follower up.  Push and pull the magazine floor plate to ensure it is properly attached to the magazine tube and undamaged.  Insert the empty magazine into an empty pistol with the slide locked back and press the slide stop lever down.  Pull the slide completely to the rear.  The empty magazine should lock the slide back.  Test all magazines in this manner.