Care and Maintenance for PolyStinger Flashlight

* FLASHLIGHT MUST BE CHARGED OVERNIGHT BEFORE FIRST USE *

Safety

- The Poly/Stinger is not approved for use in hazardous atmospheres.  DO NOT attempt to use these in areas requiring explosion proof lighting.

- SAVE THESE INSTRUCTIONS.  This manual contains important safety, operating and maintenance information for your Stinger and charger.

- Before using the charger, read all instructions and cautionary markings on the charger.

- Caution: To reduce risk of fire, electrical shock, or personal injury, do not attempt to use this charger to recharge any other product.  Likewise, do not attempt to charge the Stinger on any other charger.

- Don’t abuse the cord.  Never carry charger by the cord or yank the cord to disconnect it from a receptacle.

- Plug AC charger directly into an electrical outlet.  Do not use an extension cord.

- Do not use damaged charger.  Have damaged cords or plugs replaced immediately.

- Do not put any metal objects into the charging terminals located I the charger holder.  Although there is no electrical shock hazard, this action could cause a burn injury.

- Remove Stinger from charger holder before attempting any routine cleaning or maintenance.  Do not try to repair the unit or charger yourself.  Take it to a qualified service facility or return it to the factory.

- Use only battery #75175 or 77175 (see parts list).  The contract agreement in the Stinger precludes the use of other batteries.  Dispose of worn out or damaged batteries properly.  Do not attempt to incinerate the battery as it may explode in a fire.  Handle the battery carefully and newer allow it to short circuit.

- A small leakage of liquid from the battery cells may occur under extreme usage or high temperature.  This does not necessarily indicate a failure.  However, if the outer case seal is broken and liquid gets on your skin:

      - Wash promptly with soap and water.

      - Neutralize with a mild acid, such as lemon juice

      - If battery liquid gets into your eyes, flush them with clear water for a minimum of the (10) minutes and seek immediate medical attention.  (Medical note: the liquid is a 25-25% solution of potassium hydroxide.)

- Caution:  The Stinger’s xenon bulb is pressurized.  Wearing safety glasses is recommended during bulb replacement.  The bulb gets extremely hot.  Do not touch a lighted bulb with your bare fingers.

- Use this product for other than a lighting device is not recommended.  Streamlight specifically disclaims liability for other than recommended use.

Charging

Fully charge your Stinger before first use.  Several charge/discharge cycles may be necessary to achieve full battery capacity.  The Stinger is designed to be left in the charger continuously when not in use.  This will ensure the Stinger is always ready for use, and there is no danger of overcharge.  See Care and Use of Nickel-Cadmium Batteries for additional battery information.

To charge the Stinger, first turn off and insert it into the charger.  The LED in the charger should light, indicating charge current is flowing.  A full charge will take approximately ten (10) hours, 2.5 hours for fast charging. The Stinger should run for more than one (1) hour after a full charge.

Note:  Leaving the lamp on after it becomes noticeably dim can reduce the useful life of the battery.

Bulb Replacement

- Use only Sthinger replacement #75914 for Stinger, Stinger XT and PolyStinger.  A spare bulb is stored in the tail cap in Stinger and PolyStinger.

- Allow the Stinger bulb to cool before attempting replacement.  Wear eye protection.

- Before working on the Stinger, remover the tail cap and battery.

- Unscrew and remove the face cap/reflector assembly and the focus spring in the UltraStinger.  This will expose the bulb and the front of the switch module.

- Remove the old bulb by pulling on the glass.  Observer the relationship of the bulb pins to the contact holes in the switch module.

- Insert the pins of the new bulb into the small slats to the inside of the contacts in the switch module, and push the base of the bulb against the switch module, taking care not to bend the pins.  Wipe the bulb clean of fingerprints.

- Replace the face cap/reflector, battery and tail cap.  Turn the Stinger “on” and check the focus.  If satisfactory focus cannot be obtained by turning the face cap, the bulb is probably not on center.  Turn off the Stinger and lock into the reflector to see if the bulb is offset to on side.  Be Careful, the bulb will be hot.  Remove the face cap/ reflector and gently push the bulb towards cent. Replace the face cap/reflector and recheck the focus.

Care and Use of Nickel-Cadmium Batteries

In order to obtain the maximum performance and life from the nickel-cadmium batteries supplied with the Stinger:

- Thoroughly read the sections in the manual covering Safety, Charger Mounting and Charging.

- Fully charge the Stinger before first use.

- Although the Stinger is designed to be left on charge continuously, there is an exception: if the surrounding temperature is below 10 degrees F, continuous charging is not recommended.

- There are special considerations to note when using multi-cell rechargeable nickel-cadmium batteries, such as found In the Stinger.  If a nickel-cadmium battery is subjected to repeated and extensive overdeep discharges, such as an aggressive conditioning procedure to eliminate “memory” which runs the battery down completely on a regular basis, it can experience a voltage reversal of one of the individual cells.  This may cause a buildup of pressure within the cell which can lead to venting of the electrolyte, cell damage and early battery failure.  In addition, should the pressure relief vent on the top of the battery become damaged, this pressure increase could cause the cell to burst, causing damage to the Stinger, and possible personal injury.

- To obtain the safest and largest service from your rechargeable products, Streamlight, in conjunction with the leading manufactures of nickel-cadmium batteries, offers the following recommendations:

  - Do not periodically “condition” or “exercise” your flashlight battery despite what you may have been told about nickel-cadmium “memory.”  According to the most recent technical manuals of battery manufacturers, the actual existence of “memory” I  a battery used under the conditions of flashlight service is extremely unlikely.  Streamlight specifically discourages a regular ritual of deep discharging, which is not only unnecessary, but will greatly shorten lamp and battery life.

  - If the battery is overdischarged, there may be a small leakage of alkaline electrolyte from the safety vent on top of the cell.  If appears as a powdery substance and can affect the integrity of the electrical contact.  We recommend that your battery be periodically inspected and the contact area wiped clean should any electrolyte be present.  Use caution when handling a battery that has leaked.  The electrolyte is a strong caustic and can burn or irritate the skin and eyes.

WARNING:	Be sure to use genuine Streamlight replacement parts.  Use of another manufacturer’s replacement parts could affect product performance.

NOTE:	The rechargeable battery contained in this product is recyclable.  At the end of its useful life, under various country and state laws, it may be illegal to dispose of this battery in the municipal solid waste stream.  Check with your local solid waste officials for details in your area for recycling options or proper didposal.